## Slide 1
SIMPLIS Debug Report
When to use,
How to create
&
How to read
Simulation Software for Power Electronics
Component Design • Circuit Design • System Design

## Slide 2: SIMPLIS Debug Report – When is this report helpful?
If everything is going well, you don’t need this report
However, if your simulation gets stuck, bogged down, errors out before normal completion or runs far slower than it should…

## Slide 3: SIMPLIS Debug Report – How to Create Debug Report
The SIMPLIS Debug Report generator requires that simulation debug information has been explicitly requested for a previous simulation.
To turn ON Debug Info
  Put the following statement into the F11 window of the top-level SIMPLIS schematic:
      .options max_debug_data_size=10
  Run the simulation
Then, choose Simulator | Debug Simulation

## Slide 4: SIMPLIS Debug Report – CAUTION
The size of the SIMPLIS .dbg file can be set to be as large as you want (until you run out of hard disk space)
The larger the .dbg file, the larger the file size of the Debug Report, and the longer it will take to generate
In general, only request debug information for schematics that are misbehaving, remove the .OPTION statement when done

## Slide 5: Debug Report – Secret Decoder Ring
*** DEBUG PARSER PARAMETERS:
*** numevents:20
*** minuqpct :50
*** minwin :1n
*** mintc :-50
*** maxtcjump:5

## Slide 6: Debug Report – Secret Decoder Ring (1)
*** DEBUG PARSER PARAMETERS:
*** numevents:20
*** minuqpct :50 %
*** minwin :1n
*** mintc :-50
*** maxtcjump:5
The Debug Report looks for 3 types of problems:
Chattering: True if
Number of Unique events ≤ minuqpct % * numevents
&&
Time interval for numevents events to occur ≤ minwin (s)
The smallest Time Constant during any event TC ≤ mintc
A jump in value of TC ≥ maxtcjump while TC ≤ mintc

## Slide 7: Debug Report – Secret Decoder Ring (2)
T: 5.0245280684906833e-005; DELTA: 7.809421623893072e-007; TC: -21; S: 2 !R$R2(2), 4 !R$R3(2); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
T: 5.0374696344769413e-005; DELTA: 1.294156598625795e-007; TC: -64; S: 2 !R$R2(3), 4 !R$R3(3); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
T: 5.0245280684906833e-005; DELTA: 7.809421623893072e-007;
T: 5.0374696344769413e-005; DELTA: 1.294156598625795e-007;
Time (in seconds) of each event
Delta Time (in seconds) between current and previous event

## Slide 8: Debug Report – Secret Decoder Ring (3)
T: 5.0245280684906833e-005; DELTA: 7.809421623893072e-007; TC: -21; S: 2 !R$R2(2), 4 !R$R3(2); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
T: 5.0374696344769413e-005; DELTA: 1.294156598625795e-007; TC: -64; S: 2 !R$R2(3), 4 !R$R3(3); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
TC: -21; S: 2 !R$R2(2), 4 !R$R3(2);
TC: -64; S: 2 !R$R2(3), 4 !R$R3(3);
Smallest Time Constant (TC) in current PWL Topology --
TC in log(base 2)
All PWL elements that changed state to create this current topology
Index of PWL RefDes
PWL RefDes(state)

## Slide 9
ID
vD
1
2
3
Diode
ID
vDS
1
3
4
NMOS
Q
V
1
2
3
Vout
t
1
2
Comparator
Simple Switch
- OFF
- ON
PWL Segment number for different devices
Capacitor

## Slide 10: Debug Report – Secret Decoder Ring (4)
T: 5.0245280684906833e-005; DELTA: 7.809421623893072e-007; TC: -21; S: 2 !R$R2(2), 4 !R$R3(2); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
T: 5.0374696344769413e-005; DELTA: 1.294156598625795e-007; TC: -64; S: 2 !R$R2(3), 4 !R$R3(3); ***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
***NEW TOPOLOGY *** SV: 0 V(C1), 2 I(V1), 1 V(V1)
Indicates a first encounter of new combination of states
State Variables in descending order of greatest impact on small time constants
State Variable: Voltage on C1
State Variable Index

## Slide 11: Debug Report – Example 1
*** DEBUG PARSER PARAMETERS:
*** numevents:20
*** minuqpct :50 %
*** minwin :1n
*** mintc :-50
*** maxtcjump:5
Chattering – SIMPLIS is repetitively cycling through the same PWL states in a very short time period:
Chattering: True if
Number of Unique events ≤ minuqpct % * numevents
&&
Time interval for numevents events to occur ≤ minwin (s)
Number of Unique events ≤ 50% * 20 = 10
Number of Unique events ≤ 10
&&
Time interval for 20 events to occur ≤ 1n (s)

## Slide 12: Debug Report – Example 2
*** DEBUG PARSER PARAMETERS:
*** numevents:20
*** minuqpct :50 %
*** minwin :1n
*** mintc :-50
*** maxtcjump:5
The smallest Time Constant during any event TC ≤ mintc
Report tracks transitions from
TC > mintc to TC ≤ mintc
and from
TC ≤ mintc to TC > mintc
Report will output 20 events either side of these transitions
When TC1 > -50 then TC2 ≤ -50
Or
When TC1 ≤ -50 then TC2 > -50

## Slide 13: Debug Report – Example 3
*** DEBUG PARSER PARAMETERS:
*** numevents:20
*** minuqpct :50 %
*** minwin :1n
*** mintc :-50
*** maxtcjump:5
3) IF TC ≤ mintc && |TC1 – TC2| ≥ maxtcjump
Report will output 20 events either side of this transition
IF TC ≤ -50 && |TC1 – TC2| ≥ 5